J599 Series Fiber Optical Connectors

Features:

Comply with GJB599A (MIL-DTL-38999) Ⅲ series interface

Shells made of different materials and plating applicable for different environments

Five-keyway orientation with blind mating and anti-mismating function

Three-start thread quick coupling with anti-loose structure

Optical alignment using ceramic pin and ferrule to realize precise mating

Various termination option

Adaptor (hermetic type optional) without optical cable bondage

Q/21EJ841 applied enterprise standard

Performance Specifications:

| Parameter | Unit | ≤4 cores | 5~8 cores | ≤9~12 cores | ≤13～30 cores | ≤31~61 cores |
| --- | --- | --- | --- | --- | --- | --- |
| Insertion Loss | dB | ≤0.6 | ≤1.0 | ≤1.3 | ≤1.5 | ≤1.8 |
| Vibration | dB | 10～500Hz, acceleration 98m/s2 |
| Shock | --- | 980m/s2 |
| Durability(cycles) | --- | 500 |
| Tensile Strength | --- | ≥800N |
| Operating Temperature | ℃ | -55 ~ +85 |
| Heat Damp | --- | Temperature(＋30±2)℃~(＋60±2)℃, Humidity 90%～95%, Duration 4d |
| Note: Any specific requirements, please ask for customization. |

Insert Arrangement: (view from pin insulator interface)

Outline Dimensions: (Plug assemblies)

Square Flange Receptacle Assemblies:

Nut mounting Receptacle Assemblies:

Square Flange Adapter Receptacle:

Jam Nut Adapter Receptacle:

J599III Series Optical Connector Can Be Ordered In The Form Of Optical Cable Assembly

I Type Optical Cable Assembly (Outline Figure)

II Type Optical Cable Assembly (Outline Figure)

III Type Optical Cable Assembly (Outline Figure)

Telecommunication System Link Type:

Link Type 1

Link Type 2

Link Type 3